oneM2M Technical Report Document Number oneM2M-TR-0003-Architecture_Analysis_Part_2-V-0.5.0 Document Name: Architecture Analysis - Part 2: Study for the merging of architectures proposed for consideration by oneM2M Date: 2013-Jul-28 Abstract: Technical analysis for the merging of existing M2M-related Architecture work undertaken by the oneM2M Type 1 Partners This Specification is provided for future development work within oneM2M only. The Partners accept no liability for any use of this Specification. The present document has not been subject to any approval process by the oneM2M Partners Type 1. Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices. About oneM2M The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide. More information about oneM2M may be found at: http//www.oneM2M.org Copyright Notification No part of this document may be reproduced, in an electronic retrieval system or otherwise, except as authorized by written permission. The copyright and the foregoing restriction extend to reproduction in all media. © 2013, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TTA, TTC). All rights reserved. Notice of Disclaimer & Limitation of Liability The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied. NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

Contents

1	Scope	3

2	References	3

2.1	Normative References	3

2.2	Informative References	3

3	Definitions abbreviations and acronyms	4

3.1	Definitions	4

3.2	Abbreviations	4

3.3	Acronyms	4

4	Conventions	4

5	Analysis of Functional Entities	5

5.1	Existing Functional Entities: ATIS, ETSI, TIA	5

6	Analysis of existing Reference Points	6

6.1	Reference Point analysis	6

6.2	Reference Point vs Functions	9

7	Analysis of architecture styles	9

7.1	REST	9

7.2	SOAP	10

8	Conclusions	10

History	11

# 1	Scope

The present document provides an evaluation of existing M2M-related Architecture work undertaken by the founding partners of oneM2M, including: the Association of Radio Industries and Businesses (ARIB) and the Telecommunication Technology Committee (TTC) of Japan; the Alliance for Telecommunications Industry Solutions (ATIS) and the Telecommunications Industry Association (TIA) of the USA; the China Communications Standards Association (CCSA); the European Telecommunications Standards Institute (ETSI); and the Telecommunications Technology Association (TTA) of Korea.  Common Functional Entities and Reference Points are identified, as well as critical differences.  New functionality will not be considered as part of this study.

The present document is intended to ensure a common understanding of existing M2M Architectural approaches, in order to facilitate future normative work resulting in oneM2M Technical Specifications.

The present document has been prepared under the auspices of the oneM2M Technical Plenary, by the oneM2M Architecture Working Group.

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative References

The following referenced documents are necessary for the application of the present document.

Not applicable.

## 2.2	Informative References

The following referenced documents from non-Partners of oneM2M provide additional information for the analysis provided within the present document.

[i.1]	oneM2M Drafting Rules.

[i.2]	oneM2M TR-0002: "Architecture Analysis Part 1".

[i.3]	3GPP2 X.P0068: "Network Enhancements for Machine to Machine) that relate to the architectural enhancements and deployment models for supporting Machine to Machine services in 3GPP2 networks".

[i.4]	ATIS Machine to Machine (M2M) Committee

[i.5]	ETSI Machine to Machine (M2M) Committee

[i.6]	IETF draft-ietf-core-coap: "Constrained Application Protocol (CoAP)".

[i.7]	OMA Lightweight M2M

[i.8]	OMA-DM (OMA): "OMA Device Management".

[i.9]	Fielding, R.T., (2000), Dissertation: "Architectural Styles and the Design of Network-based Software Architectures, Chapter 5 - Representational State Transfer (REST)".  University of California Irvine

[i.10]	TIA TR-50 - M2M: "Smart Device Communications".

# 3	Definitions Abbreviations and Acronyms

## 3.1	Definitions

For  the present document, the following terms and definitions apply:

-none-

## 3.2	Abbreviations

For the present document, the following abbreviations apply:

-none-

## 3.3	Acronyms

For the present document, the following acronyms apply:

3GPP	3rd Generation Partnership Project

AAA	Authentication, Authorization and Accounting

API	Application programming Interface

ARIB	Association of Radio Industries and Businesses (JP)

ASP	Application Service provider

ATIS	Alliance for Telecommunications Industry Solutions

CCSA	China Communications Standards Association

CoAP 	Constrained Application Protocol

CoRE	Constrained Restful Environments

DA	Device Application

DSCL	Device Service Capability Layer

ETSI	European Telecommunications Standards Institute

GA	Gateway Applications

GSCL	Gateway Service Capability Layer

HATEOAS 	Hypermedia As The Engine Of Application State

HTTP 	HyperText Transfer Protocol

IETF 	Internet Engineering Task Force

IF	Interface

M2M	Machine to Machine (communications)

MAS	M2M Authentication Server

MSBF	M2M Service Bootstrap Function

MSP	Machine to Machine Service Provider

MTC	Machine Type Communication

NA	Network Applications

NSCL	Network Service Capability Layer

NW	Network

OMA LWM2M	Open Mobile Alliance - Light Weight M2M

OMA	Open Mobile Alliance

PoA	Point of Attachment

REST	Representational State Transfer is a style of API interface

RPC	Remote Procedure Call

SOAP	Simple Object Access Protocol

TIA	Telecommunications Industry Association

TTA	Telecommunications Technology Association

TTC	Telecommunication Technology Committee

WSDL	Web Service Description Language

XML	Extensible Markup Language

# 4	Conventions

The key words "Shall", "Shall not", "May", "Need not", "Should", "Should not" in the present document are to be interpreted as described in the oneM2M Drafting Rules [i.1].

# 5	Analysis of Functional Entities

## 5.1	Existing Functional Entities: ATIS, ETSI, TIA

This clause provides a comparative analysis of existing  ATIS M2M [i.4], ETSI M2M [i.5], and TIA TR-50 [i.10], functional architectural entities.

Table 5.1 provides a comparative matrix of the functional architectural entities supported by each architecture.

Table 5.1: TIA, ATIS, and ETSI M2M Functional Entity Comparative Matrix

| Functional Entity | TIA TR-50 | ATIS | ETSI M2M |
| --- | --- | --- | --- |
| M2M Service Capability hosted in the network domain | Yes Server Container | Yes Service Capabilities | Yes Network Service Capability Layer (NSCL) |
| M2M Service Capability hosted on an intermediary node | Yes PoA Container | No | Yes Gateway Service Capability Layer (GSCL) |
| M2M Service Capability hosted on an M2M Device | Yes PoA Container | No | Yes Device Service Capability Layer (DSCL) |
| Applications in the network domain | Yes home applications | Yes Applications | Yes Network Applications (NA) |
| Applications in the intermediary node | Yes Node Application | No | Yes Gateway Application (GA) |
| Applications in the M2M Device | Yes PoA Application | No | Yes Device Application (DA) |
| M2M Network | Yes Server | Yes Network Service Functions | Yes Network Domain |
| M2M intermediary node | Yes PoA Device | No | Yes M2M Gateway |
| M2M Device | Yes PoA Device | Yes Device | Yes Device with Service Capabilities (D) Device without Service Capabilities (D') Legacy non-ETSI Device (d) |
| AAA Server | Yes AAA-SD | No | Yes M2M Authentication Server (MAS), M2M Service Bootstrap function (MSBF) |

NOTE:	Functional Elements depicted in this figure may be placed anywhere, not necessarily outside the Access/Core network. The role/placement of AAA Server is for further study.

Figure 5.1: TIA, ATIS, and ETSI M2M Functional Architectural Entities

Figure 5.1 provides a high level overview of the common components when examining TIA TR-50 [i.10], ETSI M2M [i.5], and ATIS M2M [i.4] functional architectural entities.

# 6	Analysis of existing Reference Points

## 6.1	Reference Point analysis

This clause provides a comparative analysis of existing TIA TR-50 [i.10], ETSI M2M [i.5], and ATIS M2M [i.4], architectural reference points. Figure 6.1 shows the reference points from each source consolidated into a single functional architecture. Table 6.1 provides a comparative matrix of the reference points supported by each architecture.

Figure 6.1: TIA, ATIS, and ETSI M2M Reference Point Analysis

Figure 6.1 provides a high level architectural overview with reference points of the common components when examining TIA TR-50, ETSI M2M, and ATIS M2M functional architectural entities.

Details of the reference points are provided in tables 6.1 and 6.2. Table 6.1 also provides details of 3GPP reference points pertaining to Machine Type Communication (MTC).

Table 6.1: TIA, ETSI, ATIS, and 3GPP Reference Point Analysis for M2M

| Reference Point/Interface Description | Corresponding Reference Point | Comment |
| --- | --- | --- |
|  | TIA | ETSI | ATIS | 3GPP |  |
| M2M Device Application ↔ M2M Device Application | B5 |  |  |  |  |
| M2M Gateway Application ↔ M2M Gateway Application | B4 |  |  |  |  |
| M2M Device Application ↔ M2M Gateway Application | B3 |  |  |  |  |
| M2M Device Application ↔ M2M Network Application | B2 |  |  |  |  |
| M2M Gateway Application ↔ M2M Network Application | B1 |  |  |  |  |
| M2M Device Application ↔ M2M Device | B9 |  |  |  |  |
| M2M Gateway Application ↔ M2M Device | B3' |  |  |  |  |
| M2M Network Application ↔ M2M Device | B2' |  | * |  | * ATIS Shows an interface 'Traffic Flow (Option 2)' |
| M2M Network Application ↔ Access/Core Network Provider |  |  |  | Gi/Sgi |  |
| M2M Device Application ↔ M2M Device Service Layer |  | dIa |  |  |  |
| M2M Device Application ↔ M2M Gateway Service Layer |  | dIa |  |  |  |
| M2M Gateway Application ↔ M2M Device Service Layer | B8 |  |  |  |  |
| M2M Gateway Application ↔ M2M Gateway Service Layer |  | dIa |  |  |  |
| M2M Network Application ↔ M2M Device Service Layer | B7 |  |  |  |  |
| M2M Network Application ↔ M2M Gateway Service Layer | B6 |  |  |  |  |
| M2M Network Application ↔ M2M Network Service Layer |  | mIa | ASP IF |  |  |
| M2M Device Service Layer ↔ M2M Network Service Layer |  | mId |  |  |  |
| M2M Gateway Service Layer ↔ M2M Network Service Layer |  | mId |  |  |  |
| M2M Network Service Layer ↔ M2M Network Service Layer |  | mIm |  |  |  |
| M2M Network Service Layer ↔ M2M Device |  |  | * |  | * ATIS Shows an interfaces 'Traffic Flow (Option 1)' and 'Device Mangement' |
| M2M Network Service Layer ↔ Access/Core Network Provider |  |  | MSP IF | TSP |  |
| M2M Device ↔ M2M Device | B5' |  |  |  |  |
| M2M Device ↔ Access/Core Network Provider |  |  | NW IF |  |  |
| M2M Network Application ↔ AAA Server | A1 |  |  |  |  |
| M2M Gateway Application ↔ AAA Server | A2 |  |  |  |  |
| M2M Device Application ↔ AAA Server | A3 |  |  |  |  |
| M2M Device ↔ AAA Server | A3' |  |  |  |  |
| M2M Network Service Layer ↔ AAA Server |  | MAS/ MSBF |  |  |  |

## 6.2	Reference Points vs. Functions

Table 6.2 provides a comparative analysis of the reference points defined by TIA TR-50 [i.10], ATIS M2M [i.4], and ETSI M2M [i.5].

Table 6.2: TIA, ATIS, and ETSI M2M Comparative Reference Point Feature Matrix

| Feature | TIA TR-50 | ATIS M2M | ETSI M2M |
| --- | --- | --- | --- |
| Reference points to support M2M Service Capabilities hosted on a M2M device | Yes (B7, B8) | No | Yes (dIa,mId) |
| Reference points to support an intermediary M2M gateway/node | Yes (B1,B4,B6,B3,B3',B8, A2) | No | Yes (dIa,mId) |
| Reference points to support communication with access/core network entities | No | Yes (NW IF, MSP IF) | No |
| Reference points to support M2M Service Capabilities hosted in the network | No | Yes (MSP IF, ASP IF) | Yes (mIa,mId,mIm) |
| Reference points to support hierarchical M2M Service Capabilities on Device, Gateway and Network | No | No | Yes (mIa,mId,dIa) |
| Reference points to support direct application-to-application communication | Yes (B1, B2, B3, B4, B5) | No | No |
| Reference points to support direct device-to-device communication | Yes (B5') | No | No |
| Reference points to support communication between two instances of M2M Service Capabilities hosted in the network | No | No | Yes (mIm) |
| Reference points to support direct communication between network applications and devices and gateways (i.e. bypass M2M Network Service Capabilities) | Yes (B2') | Yes (Optional Traffic Flow option #2) | No |
| Reference points to support direct communication between network applications and M2M Service Capabilities hosted on devices and gateways (i.e. bypass M2M Network Service Capabilities) | Yes (B6, B7) | No | No |

# 7	Analysis of architecture styles

## 7.1	REST

REST stands for Representational State Transfer. It is a style of API interface. When the API of a system qualifies REST's features, we say the system is RESTful.

REST was first described by R.T. Fielding in his Doctoral Dissertation [i.9]. The basic notion of REST is resource. Any information in the oneM2M system that can be named and addressed can be a resource: a document or image, a temporal service, a collection of other resources, a non-virtual object, a fragment of data, and so on. REST can be summarised to several basic constraints.

Client to Server. Client is separated from the Server by interfaces. As long as the interface stays the same, Client and Server can evolve separately.

The interface between client and server is Stateless. The request on the interface contains all the information needed for the server to handle the request.

Cache. Cache is used to improve the scalability and performance.

Uniform Interface. The resources could be addressed by the same methods. There are four constraints about the Uniform Interface:

identification of resources;

manipulation of resources through representations;

self-descriptive messages;

hypermedia as the engine of application state (HATEOAS).

Layered system. The system is divided by several layers. Each layer provides functions to the upper layer by utilise the functions provided by the lower layer. Each layer can evolve separately.

RESTful guarantees that the client needs no prior knowledge of the server. Every client can access to the resources using uniform interfaces. The method to parse the resource is along with the resource. A REST Client can interact with the server entirely using hypermedia provided by the server, which is the concept of HATEOAS. Resources are connected with each other using links. The REST Client can navigate from resources to resources to obtain the information desired. The HATEOAS constraint serves to decouple client and server in a way that allows the server to evolve functionality independently.

More and more architecture designers have adopted RESTful architecture in the M2M area; ETSI M2M [i.5], OMA DM2.0 [i.8], OMA LWM2M [i.7], IETF CoRE CoAP [i.6], etc.

## 7.2	SOAP

Web services provide a layer of abstraction above existing software, such as application servers, messaging, and packaged applications.

Applications expose interfaces that are described in a machine process-able format, the Web Service Description Language (WSDL). It is also possible for applications to interact through SOAP interfaces which provide a means to describe message format. These messages are often transported over HTTP and encoded using XML.

SOAP is method for exchanging XML based message over the Internet for providing and consuming web services. SOAP message are transferred forming the SOAP-Envelope.

RPC (remote procedure call) is another way of providing and consuming web services. It uses XML to encode and decode the remote procedure call along with its parameters.

# 8	Conclusions

The present document offers an overview and summary of the most current standards activity related to M2M, with a goal of providing a common understanding of existing M2M Architectural approaches.

The present document may be used to facilitate future normative work resulting in oneM2M Technical Specifications.

# History

| Publication history |
| --- |
| V.1.0.0 | <dd Mmm 2013> | <Milestone: Scheduled for TP#3 – tbc> |

| Draft history (to be removed on publication) |
| --- |
| V.0.0.1 | 07 Feb 2013 | Rapporteur Input – Skeleton Draft |
| V0.0.2 | 13 Feb 2013 | Rapporteur Input – Skeleton Draft (editorial revisions) |
| V0.0.3 | 25 Feb 2013 | Rapporteur Input – Skeleton Draft (input to ARC F2F meeting) |
| V0.0.4 | 27 Feb 2013 | Rapporteur Input – Skeleton Draft (agreed during ARC F2F meeting) |
| V0.0.5 | 28 Feb 2013 | Rapporteur Input – Skeleton Draft (revised document title) |
| V0.1.0 | 11 Mar 2013 | Rapporteur Output Draft from TP#003 including following agreed documents: oneM2M-ARC-2012-0168R03 (Initial text for clause 5 and clause 6) |
| V0.1.1 | 18-Mar-2013 | Rapporteur Output Draft from ARC call 14-Mar-2013, with following revisions: 1) Added Table 6.1 and Table 6.2 from agreed document 0168R03 (these tables were inadvertently omitted from V0.1.0) 2) Added Note above Figure 5.1 re: placement of Functional Elements and AAA 3) Changed label on "M2M Constrained Device" in Figure 5.1 to "M2M Device" |
| V0.2.0 | 17-Apr-2013 | Rapporteur Output Draft from TP#004 including following agreed documents: oneM2M-ARC-2013-0250 (Introduction of REST) |
| V0.3.0 | 09-June-2013 | Rapporteur Input Draft for TP#005 based on output draft V0.2.0 from TP#004: Updated clauses 2.1, 5.1, 6.1, 6.2, & 8. Removed clauses 6.3, 8.1 through 8.5, and Annex |
| V0.3.1 | 18-June-2013 | Replaced clause 7.2 title from Web Service to SOAP. Removed editor notes related to further input from TIA. |
| V0.4.0 | 25 June-2013 | Pre-approval processing by the Secretariat |
| V0.4.0a | July 2013 | Clean-up done by editHelp! e-mail: mailto:edithelp@etsi.org |
| V0.5.0 | 28 July 2013 | Editorial Changes and editHelp suggestions Final version for TP Approval |